## Slide 1: Week 3 – Gripper
Advanced Mechatronics System Design – MANU2451
Dr Chow Yin LAI, School of Engineering
Edited by Dr Milan Simic RMIT University, Victoria, Australia Email: milan.simic@rmit.edu.au

## Slide 2: Teaching Schedule
Week |  | Class Activity Before | Lecture | Class Activity During or After
1 |  |  | Introduction to the Course / Introduction to LabVIEW | LabVIEW Programming
2 |  |  | Introduction to LabVIEW / Data Acquisition | LabVIEW Programming
3 |  |  | Gripper / Introduction to Solidworks / Safety | Gripper Design
4 |  |  | Sensors I | myRIO Programming for Sensor Signal Reading / Gripper Design
5 |  |  | Sensors II | myRIO Programming for Sensor Signal Reading
6 |  |  | Actuators I | 3D Printing
7 |  | LabVIEW Assessment. | DC Motors I | Matlab Simulink Simulation
8 |  | Design report submission | DC Motors II | Matlab Simulink Simulation / myRIO Programming for Control
9 |  |  | Actuators II | Matlab Simulink Simulation / Assemble Gripper
10 |  |  | Modeling and System Identification | Matlab Simulink Simulation / Test Gripper
11 |  |  | Artificial Intelligence I | Matlab Simulation / Finalize Gripper
12 |  | Gripper Demonstration / Submission of Report | Artificial Intelligent II | Revision

## Slide 3: Content
Introduction
Gripper Mechanism
Mechanical Components
  Motor and Coupler
  Gears
Design for 3D Printing
Safety Induction
Gripper Design Project
  Gripper Design in Team
  Fill in Safety Forms
Attachment: Quick Guide to using Solidworks

## Slide 4: Content
Introduction
Gripper Mechanism
Mechanical Components
  Motor and Coupler
  Gears
Design for 3D Printing
Safety Induction
Gripper Design Project
  Gripper Design in Team
  Fill in Safety Forms
Attachment: Quick Guide to using Solidworks

## Slide 5: Introduction to Grippers
Gripper examples:
  Two fingers https://www.youtube.com/watch?v=DW4ttbLh_kA
An integral part of robots and material handling systems.
  For gripping and grasping of object.
  E.g. for moving object from one place to another.

## Slide 6: Introduction to Grippers
Gripping methods
Surface
Suction
Magnetic
Pinning
Pinching
2-Finger
3-Finger
Enclosing
2-(big)-Fingers
Multiple Fingers
Suction Gripper for Glass
https://commons.wikimedia.org/wiki/File:KUKA_robot_for_flat_glas_handling.jpg
Suction grippers:
  Full or partial vacuum
  Local pressure in the gripper area lower than ambient pressure
  Full vacuum not suitable for porous materials
Magnetic grippers:
  Only for ferrous materials
Pinning:
  Needles pressed into object
Bernoulli Gripper
https://commons.wikimedia.org/wiki/File:Bernoulli_Gripper.png

## Slide 7: Introduction to Grippers
Gripping methods
Surface
Suction
Magnetic
Pinning
Pinching
2-Finger
3-Finger
Enclosing
2-(big)-Fingers
Multiple Fingers
Pinching gripper is the original gripper concept for robots.
Simple, robust and efficient.
The fingers are either flat-faced or have circular or v-grooves.
Two-finger flat-faced finger grippers rely solely on friction to hold the object.
Force opposing sliding along gripper surface:
  N = normal force on finger face, n = no. of fingers, and µ = coefficient of friction
Object

## Slide 8: Introduction to Grippers
Gripping methods
Surface
Suction
Magnetic
Pinning
Pinching
2-Finger
3-Finger
Enclosing
2-(big)-Fingers
Multiple Fingers
To avoid sliding, Ffriction for a two-finger gripper must satisfy the following conditions depending on direction of movement.
  Move up:
  Move down:
N
N
m(g+a)
N
N
m(g-a)
(a)
(b)

## Slide 9: Introduction to Grippers
Gripping methods
Surface
Suction
Magnetic
Pinning
Pinching
2-Finger
3-Finger
Enclosing
2-(big)-Fingers
Multiple Fingers
Enclosing grippers embraces / envelops the whole object when closed
Gripper does not pinch the object unless the object fills the gripper volume
Advantage: Handle all variations of product as long as it fits inside the gripper
Disadvantage: Does not provide exact positioning unless if object is big enough to be pinched
Object

## Slide 10: Introduction to Grippers
One of the challenges in gripper research is to create a gripper which is able to pick up unfamiliar objects with various shapes and surface properties.
Some modern “Universal” grippers:
  Granular jamming https://www.youtube.com/watch?v=ZKOI_lVDPpw
    Granular material (e.g. Coffee ground) flows around the target object and conforms to its shape.
    When vacuum is applied, the granular material contracts and hardens quickly to pinch and hold the object.
  Soft robotic gripper https://www.youtube.com/watch?v=Y5kZO8SSxVw
    Silicon rubber gripper
    Can handle delicate objects

## Slide 11: Grippers as Mechatronics System
Conventionally, grippers are rather simple devices.
  Two mechanically actuated fingers can handle many objects.
  Objects mostly made of hard material and can withstand hard pinching.
However, in recent years, there are new requirements and challenges:
  Soft, delicate and unstructured objects. E.g. food.
    Fruits, vegetables, biscuits etc. cannot be pinched tightly.
    Fruits, vegetables etc. come in different sizes and shapes.
Need sensors and control
  Force sensing and control to grab objects at suitable force without damaging it
Able to communicate with the robots
Mechatronics!!
https://www.youtube.com/watch?v=NgZqVjcI7P0

## Slide 12: Content
Introduction
Gripper Mechanism
Mechanical Components
  Motor and Coupler
  Gears
Design for 3D Printing
Safety Induction
Gripper Design Project
  Gripper Design in Team
  Fill in Safety Forms
Attachment: Quick Guide to using Solidworks

## Slide 13: Gripper Mechanism
We will focus only on two-finger grippers.
Finger trajectory:
Linear translation
Curvilinear translation
Rotation

## Slide 14: Gripper Mechanism
Possible realization of the finger motion using rotary joints:
Rotary actuation can be transformed to linear motion through rack and pinion, belt and pulleys etc. (and vice versa)

## Slide 15: Gripper Mechanism
Possible realization of the finger motion using pinion and rack:
Rack and Pinion
https://commons.wikimedia.org/wiki/File:Rack_and_pinion.png

## Slide 16: Gripper Mechanism
Possible realization of the finger motion using cam and followers joints:
Can also be circular but eccentric

## Slide 17: Gripper Mechanism
Possible realization of the finger motion using screw mechanism:

## Slide 18: Example - Gantry Robot Gripper
Sensors and Actuators
Micro switch
Electromagnetic sensor
Rotary Encoder
DC Motor
Pneumatic Valve

## Slide 19: Gantry Gripper Kinematics

## Slide 20: Large Gantry – XYZ Robot

## Slide 21: Things to Consider for Design
Weight
Lower weight for increased acceleration and reduced cycle time
Dimensions
Workpiece
Work area clearance
Range of Parts
Adjustable
Usage of inserts
Rigidity
Maintain accuracy
Reduce vibrations
Force level
Maximum force for safety / workpiece
Minimum force for gripping

## Slide 22: Things to Consider for Design
Maintenance
Should be easy and fast
Compliance
Helps guide work into out-of-alignment conditions
Sensors
Check for parts not in gripper
Gripper changer
Make a robot multifunctional
Usage environment
Protection against fluid, temperature, dust etc.
https://www.youtube.com/watch?v=gQ7-VgQXSU0

## Slide 23: Further References
  Gripper Technologies for Food Industry Robots by T. K. Lien, in Robotics and Automation in the Food Industry, Chapter 7, pp. 143-170, Elsevier Science.
  Robotic Systems by G. Onwubolu, in Mechatronics, Chapter 15, pp. 531-555, Butterworth Heinemann.
  Grasping in Robotics by G. Carbone (Ed), Publisher: Springer

## Slide 24: Content
Introduction
Gripper Mechanism
Mechanical Components
  Motor and Coupler
  Gears
Design for 3D Printing
Safety Induction
Gripper Design Project
  Gripper Design in Team
  Fill in Safety Forms
Attachment: Quick Guide to using Solidworks

## Slide 25: Review of Mechanical Components
  We saw earlier that to realize the finger pinching motion, it is often necessary to translate linear motion to rotary motion, and vice versa.
  Also, most motors which are used in mechatronics devices provide high speed but low torque / force.
    If the required gripping force is higher than what can be provided by the motor, we will need a gear to increase the torque.
    In this section, we will have a review of a few mechanical components (which you might need for the gripper design project).

## Slide 26: Motor: How to attach load onto shaft
  The motors usually have a shaft with a D-shape cross section.
  Load with hole can be secured to the motor shaft using a set screw.
Load – to make use of the rotary motion from motor
Set screw

## Slide 27: Motor: How to attach load onto shaft
  If the load doesn’t have a “pipe”-like section, then a coupler can be used to connect the load and motor.
Load – to make use of the rotary motion from motor
Set screw
Coupler

## Slide 28: Gears
Rotating machine part with teeth, meshes with another toothed part to transmit torque. Four principle types:
https://commons.wikimedia.org/wiki/File:Gear-kegelzahnrad.svg
https://commons.wikimedia.org/wiki/File:Worm_Gear.gif
Spur Gears
Teeth parallel to axis of rotation
Transmit motion from one shaft to another parallel shaft
Helical Gears
Teeth inclined to axis of rotation
Less noisy due to gradual engagement of teeth
Can be used for non-parallel shafts
Bevel Gears
Teeth formed on conical surfaces
Transmit motion between intersecting shafts
Straight tooth, spiral tooth, hypoid
Worm Gears
Worm resembles screw
Can achieve high gear ratio
Self-locking

## Slide 29: Gears
Nomenclature (Spur gear):
  Module: Ratio of pitch diameter (i.e. diameter of pitch circle) to the Number of teeth:
    Thus for different gears of same module, the diameter is proportional to the number of teeth.
Pitch circle
Addendum circle
Dedendum circle
Addendum
Dedendum
Circular pitch

## Slide 30: Gears – Speed Reduction
The most important reasons for using gears are to change the speed, torque and direction.
Speed:
  When two gears are in mesh, their pitch circles roll on one another without slipping.
  If gear 1 and 2 have pitch radii and angular velocity respectively, then the pitch line velocity is:
  Thus the relation between the radii on the angular velocities is
Base circle
Pitch circle
“Driving gear”
“Driven gear”

## Slide 31: Gears – Torque Amplification
Torque which a motor can provide is usually proportional to its size.
If high torque is required:
  Either use a big and powerful motor: Direct drive thus no backlash, but big size, heavy and costly.
  Or use a smaller motor (with lower torque) and use gears to increase the torque:
    Assume no frictional loss, then input power equals output power:
    Substitute equation from previous slide, we have:

## Slide 32: Gears – Imperfection
Efficiency
  Efficiency is the ratio of output power to input power.
  If efficiency is 100%, then the torque amplification in previous slide holds.
  However, if efficiency is less then 100%, the torque equation becomes:
Assume speed transmission is not affected by efficiency since the teeth are physically constrained to have same linear speed at point of contact

## Slide 33: Gears – Imperfection
Backlash
Backlash
https://commons.wikimedia.org/wiki/File:Backlash.svg
  Error in motion that occurs when gears change direction.
  Due to gap between trailing face of the driving tooth, and the leading face of the tooth behind it.
  Gap must be closed before force can be transmitted.

## Slide 34: Content
Introduction
Gripper Mechanism
Mechanical Components
  Motor and Coupler
  Gears
Design for 3D Printing
Safety Induction
Gripper Design Project
  Gripper Design in Team
  Fill in Safety Forms
Attachment: Quick Guide to using Solidworks

## Slide 35: Introduction to 3D Printing
3D Printing: Object is created by laying down successive layers of material until the entire object is created.
There are different technologies to 3D Printing.
  The 3D Printer which we will use makes use of the Material Extrusion technology, “Fused Deposition Modeling (FDM)”.
FDM
https://commons.wikimedia.org/wiki/File:FDM_by_Zureks.png
  Nozzle is heated to melt the material.
  The molten material is then deposited by extrusion head.
  The extrusion head is moved horizontally and vertically to build the object layer by layer.

## Slide 36: 3D Printing Materials
Most commonly used plastic material:
  ABS (Acrylonitrile Butadiene Styrene):
    Durable and strong, slightly flexible.
    Warping; Non-biodegradable.
    Needs heated base during printing.
  PLA (Polyactic Acid):
    Biodegradable, derived from renewable resources.
    Tough but brittle. Less warping issues.
Lego Bricks
https://commons.wikimedia.org/wiki/File:Lego_Color_Bricks.jpg
PLA Skull
https://commons.wikimedia.org/wiki/File:3D_Printed_Macrognathism.jpg

## Slide 37: Tips for 3D Printing Design
Minimum Wall Thickness
  ABS and PLA: 1mm
  If wall thickness is too thin:
    Fragile and break off easily. Or:
    Unable to be printed at all.
https://www.3dhubs.com/knowledge-base/pla-vs-abs-whats-difference/#what-are-abs-and-pla

## Slide 38: Tips for 3D Printing Design
Clearance:
  When printing a peg and a hole:
    If both are designed to be 3mm in diameter, most likely the peg will not fit into the hole.
    Due to printing accuracy of about 0.2mm.
    Also due to thermal expansion and contraction.
    Suggested minimum clearance: 0.6mm.

## Slide 39: Content
Introduction
Gripper Mechanism
Mechanical Components
  Motor and Coupler
  Gears
Design for 3D Printing
Safety Induction
Gripper Design Project
  Gripper Design in Team
  Fill in Safety Forms
Attachment: Quick Guide to using Solidworks

## Slide 40: Safety Declaration Form (Individual)
Everyone must complete and sign this form.
Please scan and email me in pdf form.

## Slide 41: Risk Assessment Form (Team)
This is to be completed in team.
Please scan and email me in pdf form.
Group leader
Give detail
E.g. Using drills – injury to finger (C x 3 = H)
Write as much as you think of.

## Slide 42: Risk Assessment Form (Team)
Continued…
E.g. use G-clamp instead of holding workpiece by hand. (E x 3 = M)

## Slide 43: Could Electrical Potential Kill ?
Could Potential Difference, i.e. Voltage Kill?

## Slide 44: Current Kills
Rbody ≈ 1K  = 1000 ,
    Depends on moisture, wetness
    Could be more, but much less as well!!!
Dangerous Current is 14mA = 0.014 A, More can Kill!!!
Car Battery = 12V, … DC
AC Power 240, 50Hz AC

## Slide 45: High Frequency, Voltage and Current Tesla Current
High Frequency Current travel on the surface
Not through the body

## Slide 46: Content
Introduction
Gripper Mechanism
Mechanical Components
  Motor and Coupler
  Gears
Design for 3D Printing
Safety Induction
Gripper Design Project
  Gripper Design in Team
  Fill in Safety Forms
Attachment: Quick Guide to using Solidworks

## Slide 47: Gripper Project
You will make a gripper with the following requirements:
  Position controlled
  Force controlled:
    Mechanism strong enough to pinch with force up to 50N.
    However, we use sensor and control the force in order not to break an egg!
Some parts will be given:
  DC Motor with integrated encoder
  National Instruments myRIO
  Motor driver (Sabertooth)
  IR range sensor
  Force sensor
https://commons.wikimedia.org/wiki/File:Egg_on_white_background.jpg
https://commons.wikimedia.org/wiki/File:Broken_egg_orange.jpg

## Slide 48: Gripper Project
Some info on the parts provided:
Check vendor website for datasheet, dimension, drawings
No. | Item | Details | Vendor & Part number
1 | Geared motor with integrated encoder | 172:1 Metal gearmotor; 25D x 56L mm; 6V: 56RPM & 250mA Stall: 2.48Nm & 6.5A (Suggest to use 1/3 only i.e. 0.8Nm) Encoder approximately 8246 counts per revolution | RobotGear SKU-003141
2 | Motor Driver | Sabertooth Dual 5A DC Motor Driver 5A continuous 10A peak | Littlebird DF-DRI0012
3 | Loadcell An Industrial Weighing Scale | Disc type; 5-50kg force; 20mm x 11mm | www.htc-sensor.com TAS606
5 | IR distance sensor | IR distance sensor includes cable (4-30cm) | Littlebird GP2Y0A41SK0F
6 | Breadboard | Half-Size Breadboard | Littlebird DF-FIT0096
7 | Controller | National Instruments myRIO | National Instruments

## Slide 49: Gripper Project
Components to include:
  Force sensor
  IR Range sensor
  Reflective surface
  Potentiometer (Optional)
  Motor with Encoder
Make sure 2 & 3 are not obstructed by the egg. They are used to measure the opening of gripper, not the distance to the egg!
Mechanisms, gears of your own choice
1
2
3
4
5

## Slide 50: Gripper Project
Connections:
Mechanisms, gears of your own choice
1
2
3
4
5
myRIO
DI if Encoder
AI if Potentiometer
AI
AO
Sabertooth
Amplifier
AI

## Slide 51: Gripper Project
Sample Design

## Slide 52: Gripper Project
Sample Design
Bonus will be given if your design is NOT one of these!
Make sure sensor not obstructed by egg
(Note: The motor can deliver max 2.48Nm, but it is recommended to use only 1/3 of this maximum torque. Therefore please assume a continuous torque of 0.8Nm)

## Slide 53: Gripper Project
You will:
  Form a team of 3 members
    Ideally with diversed background.
  Design a gripper.
  Purchase own standard parts (Gears, resistors, screws, washers etc.)
  Suggested places to buy materials and components:
    Shops: Bunnings, Jaycar
    Online: RS Online, Element14, Littlebird, Australianrobotics, Misumi, DFRobot, Core Electronics, Digikey
Mechanical
Computer
Electrical / Electronics
Control Systems

## Slide 54: Gripper Project
You will (continued):
  3D Print, fabricate and assemble the gripper.
  Program LabVIEW to
    Read in sensor signals (encoder, force sensor, IR measurement etc.) using NI myRIO.
    Control the motor to achieve desired outcome, i.e. Position control and force control of the gripper.
  Test and demonstrate the gripper!
  ... and submit a report at the end of the semester.
Have Fun!
Refer to Marking Rubric in Canvas

## Slide 55: Let’s Get Started!
Form the team:
  Provide name of team members.
Obtain electronic components and mechanical toolbox
  Sign and submit loan form
Risk Assessment & Safety Declaration forms.
  Discuss and complete these safety forms in team.

## Slide 56: Let’s Get Started!
Start your design, calculations etc.
  You may start with pen-and-pencil sketches first, before designing in details in Solidworks.
  Think about:
    What finger trajectory to have: Linear, Curvilinear, Rotary
    What mechanisms to use: Rotary joints, rack and pinion, cam and follower, belt and pulley etc.
    What actuation mode to use: Given the rotary motor, do you want to have pure rotary motion? Or do you want to transform the rotary motion to linear motion?
    How much should the dimension be? Gripper opening must be bigger than an egg.
    How much force is needed to break an egg? How much torque amplification is needed? What gears are needed to achieve this?

## Slide 57: Let’s Get Started!
  You are free to discuss and design until 9.30pm this evening.
Thank you and have a good evening!

## Slide 58: Content
Introduction
Gripper Mechanism
Mechanical Components
  Motor and Coupler
  Gears
Design for 3D Printing
Safety Induction
Gripper Design Project
  Gripper Design in Team
  Fill in Safety Forms
Attachment: Quick Guide to using Solidworks

## Slide 59: Quick Guide to Solidworks
These notes are for your self-study / reference only.
Create Parts
  Sketch
  Dimensions
  Extrude
  Add features
  Cuts
  Trim
  Hole wizard
  Fillet
Create Assembly
  Insert parts
  Mate

## Slide 60: Creating a Part
1. Start Solidworks
2. File  New  Choose “Part”

## Slide 61: Draw the Base
3. From the tree (Feature Manager) on the left hand side, choose the appropriate plane (here: top plane)
4. From the “Sketch” tab on the top, choose the basic shape (here: rectangle)  drag across the chosen plane
Line colors:
Blue: Under-defined
Black: Fully defined
Red: Over-defined (not solved)
Yellow: Over-definde (conflict)
Brown: Dangling

## Slide 62: Draw the Base
5. To give dimension: Click “Smart Dimension” from the top  Click on the lines (and a reference)  Key in desired value
6. Add in any other features on this “base”, and remember to add the dimensions

## Slide 63: Create the Extrusion
7. When sketch is completed, click “Exit Sketch” on the top.
Highlight “Sketch1” on the tree.
Go to “Feature” tab on the top  Select “Extruded Boss / Base”  Key in desired thickness (You can see a preview)
8. Click the “Tick” button to finish.
Notice the tree now lists “Boss-Extrude1”, with “Sketch1” at the lower level.

## Slide 64: Add Features on Surface
9. Suppose you want to add features on the top surface  Click on the surface  Right click  Select “Normal To” button
10. From the “Sketch” tab, select the desired shape  drag across the surface  Add dimension using “Smart Dimension”

## Slide 65: Add Features on Surface
11. When sketch is completed, click “Exit Sketch” on the top.
Highlight “Sketch2” on the tree.
Go to “Feature” tab on the top  Select “Extruded Cut”  Key in desired depth of cut (You can see a preview)
12. Click the “Tick” button to finish.
Notice the tree now lists “Cut-Extrude1”, with “Sketch2” at the lower level.

## Slide 66: Add Features on Surface
13. Again, to add another feature on the top surface  Click on the surface  Right click  Select “Normal To” button
14. From the “Sketch” tab, select a circle  drag across the surface  Add dimension using “Smart Dimension”

## Slide 67: Add Features on Surface
15. Add another line across the circle but closer to the straight slot
16. Click “Trim Entities” from the top  Choose “Trim to Closest”  Trim away parts of the line and the circle

## Slide 68: Add Features on Surface
17. Click “Exit Sketch” on the top.
Highlight “Sketch3” on the tree.
Go to “Feature” tab on the top  Select “Extruded Boss / Base”  Key in desired height (You can see a preview)
18. Click the “Tick” button to finish.
Notice the tree now lists “Boss –Extrude2”, with “Sketch3” at the lower level.

## Slide 69: Add Screw Holes
19. Click on the surface where you want to add in screw holes  Click on the surface  Right click  Select “Normal To” button
20. Sketch the positions of the holes (Recap: Sketch, dimension, trim)

## Slide 70: Add Screw Holes
21. We want to define those lines as “construction lines”, which are only used for construction but not to be part of features.
Right click on the lines  Select “Construction Geometry”  Notice that the lines become dashed
22. Choose “Point” from the sketch tab  place points at the end of the lines  Exit sketch

## Slide 71: Add Screw Holes
23. From “Feature” tab, select “Hole Wizard”  Select appropriate hole type, dimension etc.  “Position” Tab  Click on the points created earlier (you may need to click on the surface)  See the preview
24. Press “Tick” and we have an almost complete part.

## Slide 72: Add Fillet / Chamfer
25. We cam add fillet / chamfer to reduce the sharpness along the edges. Go to “Feature”  Fillet / Chamfer  key in desired dimension  click on the edges  “Tick”  Part complete!
Save!
26. You are encouraged to explore other features on Solidworks such as revolved bass, linear / circular pattern, mirror etc.
 Please refer reference book or resources from the internet.

## Slide 73: Create Another Part
1. We will create another part which will be fixed onto the first using screws.
Tip: If you need to find out the dimension of earlier parts, you can either check the sketch again, or use “Evaluate”  “Measure”
Save!

## Slide 74: Creating an Assembly
1. File  New  Choose “Assembly”
2. In the left hand panel, you will be prompted to choose a part to insert.  Choose the base  The part will appear and you can place it in the middle of the screen.

## Slide 75: Creating an Assembly
3. From the “Assembly” tab on top  Insert component  Choose the second part  The part will appear and you can place it anywhere suitable.
4. Now we would like to constrain the parts. For e.g. the screw holes must be aligned, and the surfaces must touch.
From the “Assembly” tab  Mate  Choose the desired mate selections (e.g. concentric, coincident)  Click on the two features to mate  Tick
Complete!

## Slide 76: Time for Gripper Design until 9.30pm
Thank you!